## Slide 1: Network Aware 5G Cloud Interactive Service ----Cloud Gaming
Tencent Future Network Lab
Wei Huang, Yunfei Zhang

## Slide 2
Tencent Cloud Gaming
  Tencent Instant Play and Tencent START
  Already started the Collaboration with three Chinese Operators to provide cloud gaming services
SonyPlayStationNow
  https://www.trustedreviews.com/opinion/what-is-playstation-now-a-guide-to-sony-s-streaming-service-2920562
Microsoft xCloud
  https://blogs.microsoft.com/blog/2018/10/08/project-xcloud-gaming-with-you-at-the-center/
Liquidsky iCDN
  https://enterprise.liquidsky.com/technology.html
Google Cloud
nVIDIA GeForce NOW
PaperSpace
Industrial Background

## Slide 3
Quick start & less local installation
  No need to download gaming software for installation thus saving the time to start, time spend include both the download and installation time
Less CPU power required for rendering
  No need to perform rendering with high-end processors
More device availability
  Game can be played in most devices even without high end processors
  Seamless switch
Less Piracy
  Games are played on or rely on cloud servers
Advantages of Cloud Gaming

## Slide 4
Cloud Gaming vs. Traditional Gaming
Volume
  30Mbps vs. 300kbps
User Client
  Any equipment with decoder vs. Need expensive GPU
Technical
  I,P frame vs. Operation instruction
Cloud Gaming v.s. Traditional Application
Cloud Gaming vs. Live streaming and video conference
Client Side
  No buffer or very small buffer vs. 2-8 seconds buffer
Delay Tolerance
  Sensitive <100ms mostly vs. Several seconds
Interactive service is regarded as a potential killer application in 5G

## Slide 5
Tencent at SA2 5G—Cloud Gaming 5G-AIS

## Slide 6
Edge DC
Central DC
Edge UPF
User Plane Function（UPF）
TMEC
Base Station
Cloud Gaming Server
Cloud Gaming Frame
Management
Cloud Gaming Video
Request/Respond
Present
                Resource Allocation in Cloud Gaming are based on IP, which can only show the city level.
Problem
If too many MEC in one city，service may occur 404 or 302
TMEC ability
Flow dyeing
Support DP of many companies
Flow dyeing
NOKIA DP
Intel DP
…
ZTE DP
Cloud Gaming with Tencent MEC

## Slide 7
Cloud Gaming System
Packeting
Server
Gaming Program
Gaming Logic
Rendering
Encode
Operation Interpretation
User Status
Source Image
Adaptive bitrate streaming
Decode
User Client
Streaming
Network Status
Operational instruction and User Status
Saliency detection
Network
Operational instruction
Rate Value

## Slide 8
Saliency Detection and Video Compression
Saliency Detection：
1 Find the region of Interest
2 Saving bandwidth without harming users ' experience
3 Reducing peak bitrate
Problem:
Huge Video Size vs. Limited Bandwidth
Delay and Jitter
High Quality and High Delay Low Quality and Low delay
Our Work:
1 Increase the detection accuracy  Saving about 30% bandwidth under same QoE
2 Reduce detection speed  only 10ms-30ms
3 Changing algorithms and rate allocation (in one frame) based on the network status
Balance between detection delay and detection accuracy

## Slide 9
Adaptive Bitrate Streaming
Network fluctuation
Traditional Methods：
Reaction lag
Difficult on Trade off between Rate and Delay
Rely on Client Buffer
To avoid large delay and guarantee quality: Video rates need to change with the network
Not applicable to cloud gaming
High rate may cause delay
Low rate may harm the quality of experience
Most users are in wireless network (60% ↑ keep increasing)

## Slide 10
 | Traditional | AI-based
Bandwidth | 25M+ (PC) 10M (Mobile) | 15M-20M (PC) <8M (Mobile)
delay>200ms | Once every 2 minute | Once every 4 minute
Score (Dealy+rate+switch frequency) | 1700+ | 2800+ (much higher)
Our Work:
AI-based method (RL) to improve accuracy in cloud gaming environment
ABR on Delay Sensitive Scenario (Without Buffer)
Collecting Network Information (both from user client and server) to predict the best video rate
Adaptive Bitrate Streaming
Environment
Rate Value
Action
Reward
Agent
Past rate
Current buffer Frame delay
RTT time
Lost rate
……
State

## Slide 11
Network Capability Exposure :
More information type reflect network status to help Reinforcement Learning  predict network performance
More frequency and more precise to help increase accuracy  to millisecond level and user level
Data Source: Client side; Server side; Network side
Goal: Predict the change of network; balance between delay and rate
Future: Need more kinds of information which can reflect the network status (from operator and MEC)
Application
Network Aware Application
Client Information (frame delay, buffer status)
Server Information (RTT time , video rate, frame rate, frame size…)
Network Information (loss rate, cell load, mobile position information…)
Uplink Channel
Direct Connect
Private Link

## Slide 12
Thank you！

## Slide 13
VIP slicing data
Common data
Server 1
5G BS1
VIP user1
Slicing user2
（application/mobile number）
Common user3~N
…
5G BS2
User Client
Network slicing channel1
Common channel
UPF2
UPF1
Server 2
Transport Network
Core network
5G network slicing for Cloud Gaming
3 slicing modes
Mobile number
application
position
1 Enhancing the experience of cloud gaming, reduce latency
2 Provide classified protection to users according to the different needs